1. given x, y, ya, z, penalty.
2. update x so that it is feasible for bounds and any linear constraints.
3. evaluate f, c, g, J and compute norm_c, max_infeas_bar, merit
4. iterate = 0, make sure blow-up is not signified
5. BEGIN (main loop)
6. if ( reverted ) then
  revert = .false.
  best_mults = 0
  mults_used = 'R'
  goto 17
  end
7. if ( step_accepted .or. iterate = 0 ) then
  compute residuals C_RES_l, C_RES_u, A_RES_l, A_RES_u, X_RES_l, X_RES_u.
  end
8. compute J'y and A'ya
9. check_optimal at nlp%X with multipliers from nlp%Y, nlp%Y_a, nlp%Z.
10. compute optimal_measure_curr.
11. if ( iterate = 0 ) then goto 16 end
12. compute J'y_p and A'ya_p
13. check_optimal at nlp%X with multipliers from predictor subproblem solution.
14. compute optimal_measure_pred.
15. if ( sqp_computed ) then
  compute J'y_s and A'ya_s
  check_optimal at nlp%X with multipliers from SQP subproblem solution.
  compute optimal_measure_sqp
  if ( optimal_measure_sqp <= 10 * min( optimal_measure_pred, optimal_measure_curr ) ) then
  best_mults = 3
  mults_used = 'S'
    update nlp%Y, nlp%Ya, nlp%Z, primal_vl, dual_vl, comp_vl, optimal_measure from SQP info.
    update infnorm_Y, Jtv, and Atv with the appropriate data from SQP data.
  1. end
  elseif ( optimal_measure_predictor <= 10 * optimal_measure ) then
  best_mults = 2
  mults_used = 'P'
  update nlp%Y, nlp%Ya, nlp%Z, primal_vl, dual_vl, comp_vl, optimal_measure from predictor info.
  update infnorm_Y, Jtv, and Atv with the appropriate data from predictor data.
  else
  best_mults = 1
  mults_used = 'C'
  update primal_vl, dual_vl, comp_vl, optimal_measure from current data info.
  update infnorm_Y, Jtv, and Atv with the appropriate data from current data.
  end
16. Test for convergence.
17. Possibly print debugging info for all optimality stuff from steps 6-16.
18. If ( optimal .or. iterate = max_iterate ) then go to 20 endif
19. if ( check_approximate_minimization ) then
  call check_subproblem_optimal based on nlp%X, nlp%Y, nlp%Ya, and nlp%Z.
  if ( sub_primal_vl <= sub_stop_p .and. sub_dual_vl <= sub_stop_d .and. .....etc. ) then
    merit_first_order = .true.
    if ( NM%active ) then
      set NM%fails = 0 and NM%active = .false.
    end
    if ( norm_c <= eta ) then
      decrease eta and update sub_stop_p, sub_stop_d, and sub_stop_c.
      set change_penalty = ' same'
    else
      update sub_stop_p, sub_stop_d, and sub_stop_c.
      increase penalty parameter
      set change_penalty = 'increase'
      reevaluate merit function
    end
  else
    merit_first_order = .false.
  end
  possibly print summary of sub_optimal_check.
1. end
1. print main summary line: iterate, penalty, merit, primal_vl, dual_vl, comp_vl.
2. if (optimal .or. iterate = max_iterate) EXIT
3. iterate = iterate + 1
4. If ( NM%steps > 0 .and. nlp%m > 0 .and. ~NM%active ) then
  IF ( want to turn nonmonotone on ) then
    NM%active = .true.
    save X, Y, Ya, Z, F, G, C, Jval, Ax, Bval, Hval?, merit.
    save penalty, norm_c, TRpred, max_infeas_bar, primal_vl, dual_vl, comp_vl.
    save C_res_l, C_res_u, A_res_l, A_res_u, X_res_l, X_res_u.
  end
  end
5. Set steering_good = .false. and need_best_linear = .true.
6. While ( ~ steering_good ) do
  Compute predictor step s_p, inf_norm_s_p, and inf_norm_Y_s_p.
  Compute c+J s_p, norm_c_linearize, and change in linear violation dec_con_viol_s_p.
  if ( nlp%m =0 .or. ( data%NM%active .and. data%NM%fail > 0 ) ) then
    steering_good = .true.
    goto 711
  end
  If ( norm_c_linearize = 0 ) then
    If ( s_p satisfies the second condition ) then
      steering_good = .true.
    end
  else
    if ( need_best_linear ) then
      Compute steering direction s_steer
      Set need_best_linear = .false.
    end
    Compute c+J s_steer, lin_con_vl_s_steer, and decrease_con_viol_s_steer
    if ( lin_con_viol_s_steer = 0 ) then
      increase penalty
    elseif ( dec_lin_con_viol_s_p >= factor * dec_lin_con_viol_s_steer ) then
      if ( s_p satisfieds the second condition ) then
        steering_good = .true.
      else
        increase penalty
      end
    else
      increase penalty
    end
  end
  if ( steering_good = .false. ) then
    redefine QPpred%X, QPpred%Y, QPpred%Ya, QPpred%Z, QPpred%G.
  end
  711 continue
  end while
7. Compute decrease in convex model decreaseB from norm_c, norm_c_linearize. penalty, B, G, and s_p.
8. Re-evaluation the merit function since the penalty parameter may have changed.
9. Evaluate H at nlp%X and either nlp%Y or QPpred%Y(:nlp%m).
10. If ( s_p^T H s_p <= s_p^T B s_p ) then
  alpha_c = 1
  else
  compute necessary info for computing alpha_c.
  call routine get_cauchy_step to get value for alpha_c.
  end
11. inf_norm_s_c = alpha_c * inf_norm_s_p
12. Define s_c = alpha_c * s_p.
13. Compute c+J s_c, norm_c_linearize (return set of violated and satisfied constraints) and decreaseH_cauchy.
14. Decide whether we want to compute an SQP step : sqp_computed.
15. IF (sqp_computed ) then
  Compute A s_c, Ax+A s_c, w_k needed in the descent constraint, and the descent constraint.
  Decide on what level of "SQP correction" to use and compute relevant quantities.
  Solve for SQP step s_s and compute inf_norm_s_s.
  Check descent constraint status : descent_constraint_status.
  If ( descent_constraint_status = 'FX-U' ) then
    adjust the SQP multipliers in QPsqp%Y, QPsqp%Ya, and QPsqp%Z.
  end
  Compute inf_norm_Y_s.
  Define full step s_f = s_c + s_s and inf_norm_s_f.
  Compute J s_f, norm_c_linearize, H s_f, and decreaseH_full.
  if ( decreaseH_full >= factor * decreaseH_cauchy ) then
    sqp_good_dec = .true.
    sqp_ratio_used = .true.
  else
    sqp_good_dec = .false.
    if ( NM%active .and. NM%num_fail ~= 0 ) then
      sqp_ratio_used = .true.
    else
      sqp_ratio_used = .false. DPR: ???
    end
  end
  else
  s_s = 0, inf_norm_s_s = 0, inf_norm_Y_s = 0, s_f = s_c, inf_norm_S_f = inf_norm_S_c.
  Set decreaseH_full = decreaseH_c and descent_constraint_status = 'NA'
  set sqp_good_dec = .false. and sqp_ratio_used = .false.
  end
16. if ( sqp_ratio_used ) then
  evaluate fnew, cnew, norm_cnew, and meritnew at nlp%X + s_f
  if ( NM%active ) then
    if ( NM%num_fail = 0 ) then
      NM%decreaseH = decreaseH_full
    end
    ratio = ( revert%merit_revert - meritnew ) / NM%decreaseH
  else
    ratio = ( merit - meritnew ) / decreaseH_full
  end
  else
  evaluate fnew, cnew, norm_cnew, and meritnew at nlp%X + s_c
  if (NM%active ) then
    NM%decreaseH = decreaseH_cauchy
  end
  ratio = ( merit - meritnew ) / decreaseH_cauchy
end
1. if ( ratio >= extreme_successful ) then
  success_string = 'extreme'
  success = 3
  elseif ( ratio >= very_successful ) then
  success_string = 'very'
  success = 2
  elseif ( ratio >= successful ) then
  success_string = 'success'
  success = 1
  else
  success_string = 'failure'
  success = 0
  end
2. If ( blow-up ) then
  blow_up = .true.
  else
  blow_up = .false.
  end
3. if ( NM%active ) then
  if ( success >= 1 .and. ~blow_up ) then
    NM%num_fail = 0
    NM%active = .false.
    step_accepted = .true.
    num_consec_blow_up = 0
  else
    NM%num_fail = NM%num_fail + 1
    if ( NM%num_fail <= NM_steps ) then
      step_accepted = .true.
    else
      NM%revert = .true.
      step_accepted = .false.
      num_consec_blow_ups = num_consec_blow_ups + 1
    end
  end
  else
  if ( success >= 1 .and. ~blow_up ) then
    step_accepted = .true.
    num_consecutive_blow_up = 0
  else
    step_accepted = .false.
    if ( blow_up ) then
      num_consecutive_blow_up = num_consecutive_blow_up + 1
    end
  end
  end
4. Print summary of predictor, cauchy, sqp subproblems, and step data.
5. If ( NM%revert ) then
  NMactive = .false. NM%num_fail = 0
  reset : X, Y, Ya, Z, F, C, G, Jval, Ax, Bval, Hval?, merit, norm_c, TRpred, max_infeas_bar, penalty.
  decrease TRpred.
  goto number 42
  end
6. IF ( ~step_accepted ) then
  if ( success = 0 ) then
    decrease TRpred
  else
    look into this ??? DPR ?
  end
  else
  if ( sqp_ratio_used ) then
    if ( B_type = 3 ) then
      compute BFGS%gradLx using multipliers from SQP subproblem.
    end
    nlp%X = nlp%X + s_f
  else
    if (B_type = 3 ) then
      compute BFGS%gradLx using multipliers from predictor subproblem.
    end
    nlp%X = nlp%X + s_c
  end
  F = Fnew, C = Cnew, norm_c = norm_cnew, merit = merit_new
  evaluate G, J, Ax.
  if ( B_type = 3 ) then
    if ( sqp_ratio_used ) then
      compute gradLxnew based on the new X and the multipliers from the SQP subproblem.
    else
      compute gradLxnew based on the new X and the multipliers from the predictor subproblem.
    end
  end
  if ( NM%active ) then
    define TRpred
  else
    define TRpred based on level of success : success = 1,2,3 are only possibilities.
    possibly adjust max_infeas_bar
    ensure that TRpred is bigger than some RESET value...signify whether this is needed or not.
  end
  end
7. END (main loop)